CESSNA 152

ASTRON ENTERPRISES, inc.

BEFORE STARTING ENGINE

- Preflight Inspection…COMPLETE

- Seats, belts, shoulder harnesses…ADJUST AND LOCK

- Fuel shutoff valve…ON

- Radios, electrical equipment…OFF

5.   Brakes…TEST AND SET

- Circuit breakers…CHECK IN.

## STARTING ENGINE

- Mixture…RICH

- Carburetor heat…OFF (COLD)

- Prime…AS REQUIRED (up to 3 strokes; none if engine is warm).

- Throttle…OPEN 1/2 INCH (closed if engine is warm)

- Propeller area…CLEAR

- Master Switch…ON

- Ignition switch…START (release when engine starts)

- Throttle…ADJUST for 1000 RPM or less

- Oil pressure…CHECK

- Beacon and Nav lights…ON as required

- Radios…ON

## BEFORE TAKEOFF

- Parking Brake…SET

- Cabin doors and window(s) …CLOSED AND LATCHED

- Flight controls…FREE AND CORRECT

- Flight instruments…SET

- Fuel shutoff valve…ON

- Mixture…RICH (BELOW 3000 FEET).

- Elevator trim …TAKEOFF.

- Throttle…1700 RPM

- Magnetos..CHECK (RPM drop should not exceed 125 RPM on either magneto or 50 RPM differential between magnetos)

- Carburetor heat…CHECK (for RPM drop)

- Engine instruments and ammeter …CHECK

- Suction gage…CHECK

- Throttle…1000 RPM or less

- Radios…SET

- Throttle friction lock…ADJUST

- Brakes…RELEASE

## TAKEOFF

### NORMAL TAKEOFF

- Wing Flaps…0o – 10o

- Carburetor heat…OFF

- Throttle…FULL OPEN

- Elevator control…LIFT NOSE WHEEL AT 50 KIAS

- Climb speed…65- 75 KIAS

### SHORT FIELD TAKEOFF

- Wing flaps…10o

- Carburetor heat…OFF (COLD)

- Brakes…APPLY

- Throttle…FULL OPEN

- Mixture…RICH (Above 3000 feet, LEAN to  obtain maximum RPM).

- Brakes…RELEASE

- Elevator control…SLIGHTLY TAIL LOW

- Climb speed…54 KIAS (Until all obstacles are cleared.)

- Wing flaps…RETRACT slowly after reaching 60 KIAS

## ENROUTE CLIMB

- Airspeed…70-80 KIAS.

#### NOTE

IF A MAXIMUM PERFORMANCE CLIMB IS NECESSARY, USE  SPEEDS SHOWN IN THE MAXIMUM RATE OF CLIMB CHART IN SECTION 5.

- Throttle…FULL OPEN

- Mixture…RICH (Above 3000 feet, LEAN to obtain maximum RPM.)

## CRUISE

- Power…1900-2550 RPM (No more than 75% is recommended)

- Elevator trim .. ADJUST

- Mixture…LEAN

## DESCENT

- Mixture…Adjust for smooth operation (Full rich for idle power)

- Power…AS DESIRED

- Carburetor heat…Full heat as required (To prevent carburetor icing.)

## BEFORE LANDING

- Seats, Belts, Harnesses...ADJUST & LOCK

- Mixture…RICH

- Carburetor heat…ON (HOT)

## LANDING

### NORMAL LANDING

- Airspeed…60-70 KIAS (FLAPS UP)

- Wing Flaps…AS DESIRED (Below 85 KIAS)

- Airspeed…55-65 KIAS (FLAPS DOWN)

- Touchdown…MAIN WHEELS FIRST

- Landing Roll…Lower nose wheel GENTLY

- Braking…MINIMUM REQUIRED

### SHORT FIELD LANDING

- Airspeed…60-70 KIAS (FLAPS UP)

- Wing Flaps…30O (Below 85 KIAS)

- Airspeed…MAINTAIN 54 KIAS

- Power..REDUCE to idle after clearing obstacle

- Touchdown…MAIN WHEELS FIRST

- Brakes…APPLY HEAVILY

- Wing Flaps…RETRACT

BALKED LANDING

- Throttle…FULL OPEN.

- Carburetor heat…OFF (COLD)

- Wing Flaps…20O IMMEDIATELY

- Climb Speed…55 KIAS.

- Wing flaps… RETRACT (slowly)

AFTER LANDING

- Wing flaps…UP

- Carburetor heat…OFF (COLD)

- Landing\Taxi lights…OFF(if daytime)

SECURING AIRPLANE

- Parking brake…SET

- Radios, electrical equipment…OFF

- Mixture…IDLE CUT-OFF(Pulled full OUT)

- Ignition Switch…OFF

- Master Switch…OFF

- Control Lock…INSTALL