# AIRSPEEDS FOR EMERGENCY OPERATIONS

# Engine Failure After Takeoff             60  KIAS

Maneuvering Speed:

1670 LBS                            104 KIAS

1500 LBS                             98 KIAS

1350 LBS                             93 KIAS

Maximum Glide                                 60 KIAS

Landing Without Engine Power:

Wing Flaps Up                      65 KIAS

Wing Flaps Down                 60 KIAS

# ENGINE FAILURES

## Engine Failure During Takeoff Run

- Throttle…IDLE

- Brakes…APPLY

- Wing Flaps…RETRACT

- Mixture…IDLE CUT-OFF

- Ignition Switch…OFF

- Master Switch…OFF

## Engine Failure Immediately After Takeoff

- Airspeed…60 KIAS

- Mixture…IDLE CUT-OFF

- Fuel Shutoff Valve…OFF

- Ignition Switch…OFF

- Wing Flaps…AS REQUIRED

- Master Switch…OFF

## Engine Failure During Flight

- Airspeed…60 KIAS

- Carburetor Heat…ON

- Primer…IN and LOCKED

- Fuel Shutoff Valve…ON

- Mixture…RICH

- Ignition Switch…BOTH  (or START if propeller is stopped)

### FORCED LANDINGS

Emergency Landing Without Engine Power

- Airspeed…65 KIAS (Flaps Up)

60 KIAS (Flaps Down)

- Mixture…IDLE CUT-OFF

- Fuel Shutoff Valve…OFF

- Ignition Switch…OFF

- Wing Flaps…AS REQUIRED

- Master Switch…OFF

- Doors…UNLATCH PRIOR TO TOUCHDOWN

- Touchdown…SLIGHTLY TAIL LOW

- Brakes…APPLY HEAVILY

Precautionary Landing With Engine Power

- Airspeed…60 KIAS

- Wing Flaps…20o

- Selected Field…FLY OVER, noting terrain and obstructions, then retract flaps upon reaching a safe altitude and airspeed.

- Radio and Electrical Switches…OFF

- Wing Flaps…30o (on final approach)

- Airspeed…55 KIAS

- Master Switch…OFF

- Doors…UNLATCH PRIOR TO TOUCHDOWN

- Touchdown…SLIGHTLY TAIL LOW

- Ignition Switch…OFF

- Brakes…APPLY HEAVILY

### FIRES   FIRES    FIRES     FIRES

##### During Start On Ground

- Cranking…CONTINUE, to get a start which would suck the flames and accumulated fuel through the carburetor and into the engine.

If engine starts:

- Power…1700 RPM for a few minutes

- Engine…SHUT DOWN and inspect for damage.

If engine fails to start:

- Cranking…CONTINUE in an effort to obtain a start

- Fire Extinguisher…OBTAIN (have ground attendants obtain if not installed)

- Engine…SECURE

- Master Switch…OFF

- Ignition Switch…OFF

- Fuel Shutoff Valve…OFF

- Fire…EXTINGUISH using fire extinguisher, wool blanket, or dirt.

- Fire Damage…INSPECT, repair damage or replace damaged components or wiring before conducting another flight.

##### Engine Fire In Flight

- Mixture…IDLE CUT-OFF

- Fuel Shutoff Valve…OFF

- Master Switch…OFF

- Cabin Heat and Air…OFF(except wing root vents)

- Airspeed… 85 KIAS (If fire is not extinguished, increase glide speed to find and airspeed which will provide an incombustible mixture)

- Forced landing …EXECUTE (as described in Emergency Landing without Engine Power).

##### Electrical Fire In Flight

- Master Switch…OFF

- All Other Switches (except ignition)…OFF

- Vents/Cabin Air/Heat…CLOSED

- Fire Extinguisher…ACTIVATE (if available)

WARNING: After discharging an extinguisher within a closed cabin, ventilate the cabin…If fire appears out and electrical power is necessary for continuance of flight:

- Master Switch…ON

- Circuit Breakers…CHECK for faulty circuit, do not reset.

- Radio/Electrical Switches…ON one at a time, with delay after each until short circuit is localized.

- Vents/Cabin Air/Heat…OPEN when it is ascertained that fire is completely out.

### CABIN FIRE

- Master Switch…OFF

- Vents/Cabin Air/Heat…CLOSED

- Fire Extinguisher…ACTIVATE (if available)

- VENTILATE CABIN TO CLEAR AIR

- Land as soon as possible, INSPECT

### WING FIRE

- Navigation Light Switch…OFF

- Pitot Heat Switch…OFF (if installed)

- Strobe Light Switch…OFF (if installed)

- Perform a side slip to keep the flames away from the fuel tank and cabin, and land as soon as possible, with flaps retracted.

### LANDING WITH A FLAT MAIN TIRE

- Wing Flaps…AS DESIRED

- Approach…NORMAL

- Touchdown…GOOD TIRE FIRST, hold airplane off flat tire as long as possible with aileron control.