# ENGINE FAILURES

## Engine Failure During Takeoff Run

- Throttle…IDLE

- Brakes…APPLY

- Wing Flaps…RETRACT

- Mixture…IDLE CUT-OFF

- Ignition Switch…OFF

- Master Switch…OFF

## Engine Failure Immediately After Takeoff

- Airspeed…65 KIAS (Flaps Up)

60 KIAS (Flaps Down)

- Mixture…IDLE CUT-OFF

- Fuel Selector Valve…OFF

- Ignition Switch…OFF

- Wing Flaps…AS REQUIRED

- Master Switch…OFF

## Engine Failure During Flight

- Airspeed…65 KIAS

- Carburetor Heat…ON

- Fuel Selector Valve…BOTH

- Mixture…RICH

- Ignition Switch…BOTH  (or START if propeller is stopped)

- Primer…IN and LOCKED

### FORCED LANDINGS

Emergency Landing Without Engine Power

- Airspeed…65 KIAS (Flaps Up)

60 KIAS (Flaps Down)

- Mixture…IDLE CUT-OFF

- Fuel Selector Valve…OFF

- Ignition Switch…OFF

- Wing Flaps…AS REQUIRED

- Master Switch…OFF

- Doors…UNLATCH PRIOR TO TOUCHDOWN

- Touchdown…SLIGHTLY TAIL LOW

- Brakes…APPLY HEAVILY

Precautionary Landing With Engine Power

- Wing Flaps…20o

- Airspeed…60 KIAS

- Selected Field…FLY OVER, noting terrain and obstructions, then retract flaps upon reaching a safe altitude and airspeed.

- Avionics Power Switch and Electrical Switches…OFF

- Wing Flaps…FULL (on final approach)

- Airspeed…60 KIAS

- Master Switch…OFF

- Doors…UNLATCH PRIOR TO TOUCHDOWN

- Touchdown…SLIGHTLY TAIL LOW

- Ignition Switch…OFF

- Brakes…APPLY HEAVILY

### DITCHING

- Radio…TRANSMIT MAYDAY on 121.5 MHz, giving location and intentions.

- Heavy Objects (in baggage area)…SECURE OR JETTISON

- Approach…High winds, Heavy seas…INTO THE WIND

Light winds, Heavy  Swells        …PARALLEL TO SWELLS

- Wing Flaps…from 20o to FULL

- Power…ESTABLISH 300 FT/MIN DESCENT AS 55 KIAS.

#### NOTE

If no power is available, approach at 65 KIAS with flaps up or at 60  KIAS with 10o flaps.

- Cabin Doors…UNLATCH

- Touchdown…LEVEL ATTITUDE AT ESTABLISHED RATE OF DESCENT

- Face…CUSHION at touchdown with folded coat

- Airplane…EVACUATE through cabin doors. If necessary, open window and flood cabin to equalize pressure so doors can be opened.

- Life Vests and Raft…INFLATE

### FIRES   FIRES    FIRES     FIRES

##### During Start On Ground

- Cranking…CONTINUE, to get a start which would suck the flames and accumulated fuel through the carburetor and into the engine.

If engine starts:

- Power…1700 RPM for a few minutes

- Engine…SHUT DOWN and inspect for damage.

If engine fails to start:

- Throttle…FULL OPEN

- Mixture…IDLE CUT-OFF

- Cranking…CONTINUE

- Fire Extinguisher…OBTAIN (have ground attendants obtain if not installed)

- Engine…SECURE

- Master Switch…OFF

- Ignition Switch…OFF

- Fuel Selector Valve…OFF

- Fire…EXTINGUISH using fire extinguisher, wool blanket, or dirt.

- Fire Damage…INSPECT, repair damage or replace damaged components or wiring before conducting another flight.

##### Engine Fire In Flight

- Mixture…IDLE CUT-OFF

- Fuel Selector Valve…OFF

- Master Switch…OFF

- Cabin Heat and Air…OFF(except overhead vents)

- Airspeed… 100 KIAS (If fire is not extinguished, increase glide speed to find and airspeed which will provide an incombustible mixture)

- Forced Landing…EXECUTE (as described in Emergency Landing Without Engine Power).

##### Electrical Fire In Flight

- Master Switch…OFF

- Avionics Power Switch…OFF

- All Other Switches (except ignition)…OFF

- Vents/Cabin Air/Heat…CLOSED

- Fire Extinguisher…ACTIVATE (if available)

WARNING: After discharging an extinguisher within a closed cabin, ventilate the cabin…If fire appears out and electrical power is necessary for continuance of flight:

- Master Switch…ON

- Circuit Breakers…CHECK for faulty circuit, do not reset.

- Radio Switches…OFF

- Avionics Power Switch…ON

- Radio/Electrical Switches…ON one at a time, with delay after each until short circuit is localized.

- Vents/Cabin Air/Heat…OPEN when it is ascertained that fire is completely out.

### CABIN FIRE

- Master Switch…OFF

- Vents/Cabin Air/Heat…CLOSED

- Fire Extinguisher…ACTIVATE (if available)

- VENTILATE CABIN TO CLEAR

- Land as soon as possible, INSPECT

### WING FIRE

- Navigation Light Switch…OFF

- Pitot Heat Switch…OFF (if installed)

- Strobe Light Switch…OFF (if installed)