CESSNA 172RG

ASTRON ENTERPRISES, inc.

BEFORE STARTING ENGINE

Preflight Inspection…COMPLETE

Passenger Briefing…COMPLETE

Seats, Seat belts, shoulder harnesses…ADJUST AND LOCK

Brakes…TEST AND SET

Avionics power switch …OFF

CAUTION

THE AVIONICS POWER SWITCH MUST BE OFF DURING ENGINE START TO PREVENT POSSIBLE DAMAGE TO AVIONICS.

Circuit breakers…CHECK IN.

Electrical equipment, Autopilot…OFF

Landing Gear Lever…DOWN

Cowl Flaps…OPEN (Move lever out of locking hole to reposition)

Fuel Selector Valve…BOTH

STARTING ENGINE

Carburetor heat…OFF (COLD)

Primer 2 to 4 strokes. LOCK.

Propeller…HIGH RPM

Mixture…RICH

Beacon ON.

Propeller Area…CLEAR

Master Switch…ON

Throttle…PUMP once or twice; leave open ¼ inch. If engine is hot turn auxiliary fuel pump ON during start.

Ignition Switch…START (release when engine starts)

Oil pressure…CHECK.

Avionics Power Switch …ON

12. Radios…ON

BEFORE TAKEOFF

Parking Brake…SET

Seats, Seat belts, Shoulder harnesses…CHECK SECURE

Cabin Doors…CLOSED & LATCHED

Flight Controls…FREE AND CORRECT

Flight instruments…CHECK AND SET

Fuel Quantity…CHECK and SET

Auxiliary Fuel Pump…ON (check for rise in fuel pressure), then OFF NOTE:In flight, gravity feed will normally supply satisfactory fuel flow if the engine-driven fuel pump should fail. However, if a fuel pump failure causes the fuel pressure to drop below 0.5 PSI, use the auxiliary fuel pump to assure proper engine operation.

Mixture…RICH (BELOW 3000 FEET).

Fuel selector valve… RECHECK BOTH

Elevator trim and rudder trim (if installed)…SET for TAKEOFF.

Throttle…1800 RPM

- Magnetos..CHECK (RPM drop should not exceed 150 RPM on either magneto or 50 RPM differential between magnetos)

- Carburetor heat…CHECK (for RPM drop)

- Propeller…CYCLE from high to low RPM: return to high RPM (full in)

- Oil Temperature and Pressure..CHECK

- Suction gage…CHECK

- Alternator off…CHECK Ammeter

Throttle…1000 RPM or less

Throttle friction lock…ADJUST

Strobe Lights (if installed)…AS DESIRED

Radios and Avionics…SET

Autopilot (IF installed)…OFF

Wing Flaps…SET for takeoff.

Parking Brake…RELEASE

Transponder…..ALT MODE

TAKEOFF

NORMAL TAKEOFF

1. Wing Flaps…0o

2. Carburetor heat…OFF (COLD)

3. Power…FULL THROTTLE and 2700 RPM

4. Mixture… RICH (mixture may be leaned above 3000 feet to obtain max power).

5. Elevator control…LIFT NOSE WHEEL at 55 KIAS NOTE When the nose wheel is lifted, the gear motor may run 1-2 seconds to restore hydraulic pressure.

6. Climb speed…70-80 KIAS.

7. Brakes..APPLY momentarily when airborne

8. Landing Gear…Retract in climbout.

SHORT FIELD TAKEOFF

Wing flaps…0o

Carburetor heat…OFF (COLD)

Brakes…APPLY

Power…FULL Throttle and 2700 RPM

Mixture…RICH (LEAN above 3000 feet to obtain maximum power).

Brakes…RELEASE

Elevator control…SLIGHTLY TAIL LOW

Climb speed…63 KIAS (Until all obstacles are cleared.)

Landing Gear…RETRACT after all obstacles are cleared.

ENROUTE CLIMB

Normal Climb

Airspeed…85-95 KIAS.

2. Power..25 INCHES Hg and 2500 RPM

3. Fuel Selector Valve …..BOTH

Mixture…RICH (Above 3000 feet, LEAN to obtain maximum RPM.)

Cowl Flaps……OPEN as required.

Maximum Performance CLIMB

Airspeed…84 KIAS at sea level to 77 KIAS at 10,000 MSL.

2. Power..Full Throttle and 2700 RPM

3. Fuel Selector Valve …..BOTH

Mixture…RICH (Above 3000 feet, LEAN to obtain maximum RPM.)

Cowl Flaps……FULL OPEN.

CRUISE

Power..15-25 INCHES Hg., 2100-2700 RPM.

Elevator & Rudder trim (if installed) ...ADJUST

Mixture…LEAN

Cowl Flaps…..CLOSED.

DESCENT

Fuel Selector Valve-----BOTH.

Power…..AS DESIRED

Mixture…..for smooth operation (Full rich for idle power)

Carburetor heat…As required (To prevent carburetor icing.)

Cowl Flaps…..CLOSED.

Wing Flaps-----AS DESIRED (0° - 10° below 130 KIAS, 10° -30° below 100 KIAS)

NOTE: To increase rate of descent, landing gear may be extended below 140KIAS.

BEFORE LANDING

Seats, Belts, Harnesses….SECURE

Fuel selector valve……BOTH.

Landing Gear….DOWN (below 140 KIAS).

Landing Gear…. CHECK (Observe main gear down and green indicator light illuminated).

Mixture…RICH

Propeller….HIGH RPM.

Carburetor heat…ON (Apply full heat before closing throttle)

Autopilot (If installed)…OFF

LANDING

NORMAL LANDING

Airspeed…70-80 KIAS (FLAPS UP).

Wing Flaps…AS DESIRED (0° -10° below 130 KIAS, 10° - 30° below 100 KIAS.).

Airspeed…60-70 KIAS (FLAPS DOWN).

Trim….ADJUST.

Touchdown…MAIN WHEELS FIRST

Landing Roll…Lower nose wheel GENTLY

Braking…MINIMUM REQUIRED

SHORT FIELD LANDING

Airspeed…70-80 KIAS (FLAPS UP)

Wing Flaps…30° (below 100 KIAS)

Airspeed…63 KIAS (UNTIL FLARE)

Trim….ADJUST.

Power..Reduce to idle after clearing obstacle.

Touchdown…MAIN WHEELS FIRST

Brakes…APPLY HEAVILY (Don’t SKID)

Wing Flaps…RETRACT

BALKED LANDING

Power…FULL Throttle and 2700 RPM.

Carburetor heat…OFF (COLD)

Wing Flaps…20O IMMEDIATELY

Climb Speed…55 KIAS.

Wing flaps…RETRACT to 10O after reaching 65 KIAS (after clearing obstacles pitch to Vy and retract incrementally to 0°).

AFTER LANDING

Wing flaps…RETRACT

Carburetor heat…OFF (COLD)

Landing\Taxi lights…OFF(if daytime)

Cowl Flaps….OPEN.

Transponder…..STANDBY

SECURING AIRPLANE

Parking brake…SET

Avionics power switch, electrical equipment, autopilot (If installed)…OFF

Mixture…IDLE CUT-OFF(Pulled full OUT)

Ignition Switch…OFF

Master Switch…OFF

Control Lock…INSTALL

Normal and Limitations

Vso = 42 KIAS

Vs1 = 50 KIAS

Rotate = 55 KIAS and for balked landing

Vx = 67 KIAS Gear up, 63 KIAS Gear Down.

Vy = 84 KIAS

VA = 106 KIAS @ 2650 Lbs. 89 KIAS @ 1850 Lbs.

Vfe = 130 KIAS @ 10° Flaps. 100 KIAS @ 10° - 30° Flaps.

Vlo = 140 KIAS

Vle = 164 KIAS

VNO = 145 KIAS

VNE = 164 KIAS

MAX Glide = 73 KIAS

Landing Approach = 60 – 70 KIAS Flaps Down 65 - 75 KIAS Flaps UP.

Fuel …….66 Gallons Total, 62 Gallons Usable

Oil ……..8 Quart Sump, 5 Quart Min. 1 Quart in the Filter.

Weights = 1598 Lbs. Standard Empty 2658 Lbs. Max Ramp 2650 Lbs. Max Takeoff & landing

Steep Turns = 106 KIAS, Manifold / Props =18 – 20 Inches / 2400 RPM

Lazy Eights = 106 KIAS, Manifold / Props =18 – 20 Inches / 2400 RPM

Chandelles = 106 KIAS, Manifold / Props = Full Inches / Full RPM