PIPER WARRIOR II , PA-28-161

BEFORE STARTING ENGINE

- Brakes…SET

- Carburetor Heat…FULL OFF

- Fuel Selector…DESIRED TANK

# STARTING ENGINE WHEN COLD

- Throttle…1/4” OPEN

- Master Switch…ON

- Electric Fuel Pump…ON

- Mixture…FULL RICH

- Starter…ENGAGE

- Throttle…ADJUST

- Oil Pressure…CHECK

If engine does not start within 10 seconds, prime and repeat starting procedure.

# STARTING ENGINE WHEN HOT

- Throttle…1/2” OPEN

- Master Switch…ON

- Electric Fuel Pump…ON

- Mixture…FULL RICH

- Starter…ENGAGE

- Throttle…ADJUST

- Oil Pressure…CHECK

# STARTING ENGINE WHEN FLOODED

- Throttle…FULL OPEN

- Master Switch…ON

- Electric Fuel Pump…OFF

- Mixture…IDLE CUT-OFF

- Starter…ENGAGE

- Mixture…ADVANCE

- Throttle…RETARD

- Oil Pressure…CHECK

# GROUND CHECK

- Throttle…2000 RPM

- Magnetos…   max drop       175 RPM

max difference 50 RPM

- Vacuum…5.0” Hg. + .1

- Oil Temp…CHECK

- Oil Pressure…CHECK

- Annunciator Panel…PRESS TO TEST

- Carburetor Heat…CHECK

Engine is warm for takeoff when throttle can be opened without engine faltering.

- Electric Fuel Pump…OFF

- Fuel Pressure…CHECK

- Throttle…RETARD

# BEFORE TAKEOFF

- Master Switch…ON

- Flight Instruments…CHECK

- Fuel Selector…PROPER TANK

- Electric Fuel Pump…ON

- Engine Gauges…CHECK

- Carburetor Heat…OFF

- Seat Backs…ERECT

- Mixture…SET

- Belts/Harness…FASTENED

- Empty Seats…Seat belts snugly fastened

- Flaps…SET

- Trim Tab…SET

- Controls…FREE

- Doors…LATCHED

# TAKEOFF

### NORMAL

- Flaps…SET

- Trim Tab…SET

- Accelerate to 45 to 55 KIAS

- Control Wheel…Back pressure to rotate to climb attitude.

### SHORT FIELD, OBSTACLE CLEARANCE

- Flaps…25o (second notch)

- Accelerate to 52 KIAS

- Control Wheel…back pressure to rotate to climb attitude

- Maintain 52 KIAS until obstacle cleared

- Accelerate to 79 KIAS after obstacle is cleared

- Flaps…RETRACT SLOWLY

# SHORT FIELD, NO OBSTACLE

- Flaps…UP

- Accelerate to 50 KIAS

- Control Wheel…Back pressure to rotate to climb attitude.

- After breaking ground accelerate to best rate of climb speed 79 KIAS

# SOFT FIELD, OBSTACLE CLEARANCE

- Flaps…25o (Second Notch)

- Accelerate and lift off nose gear as soon as possible. Lift off at lowest possible airspeed

- Accelerate just above ground to 52 KIAS to climb past obstacle height.

- Continue climbing while accelerating to best rate of climb speed, 79 KIAS

- Flaps…SLOWLY RETRACT

### SOFT FIELD, NO OBSTACLE

- Flaps…25o (second notch)

- Accelerate and lift off nose gear as soon as possible. Lift off at lowest possible airspeed

- Accelerate just above the ground to best rate of climb speed, 79 KIAS

- Flaps…SLOWLY RETRACT

# CLIMB

- Best Rate (flaps up)…79 KIAS

- Best Angle (flaps up)…63 KIAS

- En route…87 KIAS

- Electric Fuel Pump..OFF at desired altitude

# APPROACH AND LANDING

- Fuel Selector…PROPER TANK

- Seat backs…ERECT

- Belts/harness…FASTEN

- Electric fuel pump…ON

- Mixture…SET

- Flaps…set-103 KIAS max

- TRIM to 70 KIAS

- Final approach speed (flaps 40o)…63 KIAS

- Landing Light...TURN OFF after touchdown

# STOPPING ENGINE AND PARKING

- Flaps…RETRACT

- Electric fuel pump…OFF

- Radios…OFF

- Throttle…FULL AFT

- Mixture…IDLE CUT-OFF

- Magnetos…OFF

- Master Switch…OFF

- Parking Brake…SET

- Control Wheel…SECURED WITH BELTS

- Flaps…FULL UP

- Wheel Chocks…IN PLACE

- Tie downs…SECURE